## Slide 1
Entanglement-Dynamic Topology for Robust Quantum Sensing
Finding the finite control window where sensitivity, coherence, fidelity and readout remain jointly effective.
Hang Hu · Hsu Kiang Ooi · Anguang Hu
National Research Council Canada · Defence Research and Development Canada
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 1

## Slide 2
Introduction: defence applications
Magnetic and low-frequency RF signatures resist masking and reach where optical sensing fails — exploiting them needs lab sensitivity in a fielded package.
A submerged steel hull distorts Earth’s magnetic field. MAD instruments detect the local anomaly.
GPS-denied Magnetic navigation
Anomaly maps give an unjammable position fix where satellite navigation is denied.
The hard part is not peak laboratory sensitivity — it is holding a known operating point in the field.
SBQuantum magnetic map
Source: SBQuantum, Magnetic Navigation, sbquantum.com
Magnetic anomaly detection
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 2

## Slide 3
Introduction: background information
A nitrogen-vacancy defect in diamond is an optically addressable electron spin: initialise with green light, evolve in the field, read out the fluorescence.
S = 1
Spin triplet
Zeeman splitting shifts the m = ±1 levels linearly with the field along the NV axis.
φ ∝ B·T
Phase, not amplitude
Sensitivity improves with interrogation time, so coherence is the resource that sets it.
T₂* ≈ µs
The limit to beat
Bath-induced dephasing ends free evolution in microseconds, far short of the phase budget.
Every sensitivity gain here comes from extending usable interrogation time without losing the signal.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 3

## Slide 4
Introduction: background information
A periodic train of π pulses refocuses slow bath noise and makes the sensor respond only near a chosen frequency — extending coherence and adding selectivity at once.
One XY8 block
X
Y
X
Y
X
Y
X
Y
τ
pulse spacing sets the sensing band
N blocks → 8N π pulses
At resonance: τ = 1 / (4f)
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 4

## Slide 5
Introduction: background information
In weak-field magnetometry and narrowband RF sensing, useful control resources compete with the costs of running them.
↑ signal
Phase accumulation
Deeper XY8 sequences accumulate more target phase and sharpen the filter.
↑ selectivity
Noise rejection
Dynamical decoupling suppresses environmental noise around the sensing band.
↑ cost
Errors + time
Pulse infidelity, decoherence exposure and overhead accumulate with depth.
Design objective: minimize sensitivity penalty η(τ,N) under all resource constraints—not maximize N.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 5

## Slide 6
What EDT Means in This Study
EDT maps where sensing performance and the required quantum resources remain jointly useful.
ENTANGLEMENT
Broader framework
Multi-spin entanglement may improve field response, but it also adds preparation and coherence costs.
Current study: one NV spin
Future work: coupled or entangled spins
DYNAMICS
Calculated here
XY8 reshapes the sensor response during a measurement.
τ selects the sensing frequency
N controls accumulation, selectivity, errors and duration
TOPOLOGY
Calculated here
Near-optimal set:
η(τ,N) ≤ 1.1ηmin
At 200 kHz: one connected resonant region, β₀=1, stable under timing-grid refinement
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 6

## Slide 7
Refined analysis resolves a finite, hardware-dependent control window
N=20, τ=1.25 μs
NOMINAL OPTIMUM
160 microwave pulses
N=10–34
10% OPERATING WINDOW
Within 10% of the minimum
Optimal N: 8–64
HARDWARE DEPENDENCE
Conservative to optimistic hardware
The early coarse scan suggested N=4–10. Exact resonance sampling and a denser depth sweep resolve N=20 and a broader N=10–34 near-optimal window.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 7

## Slide 8
Pulse Errors Create a Finite Optimal Control Depth
MECHANISM
Remove pulse errors
20 → 128*
~71% lower η
Remove decoherence
N stays 20; η improves ~4.8%
Remove overhead
N stays 20; <1% change
Pulse-error accumulation creates the interior optimum
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 8

## Slide 9
Results: Pulse Timing Selects the Target Sensing Frequency
DIRECT RULE
τ = 1 / (4f)
50–500 kHz
Modeled τ follows the analytic primary resonance.
Best depth
N = 8 → 20
The 10% window changes with band.
Timing tracks the sensing band
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 9

## Slide 10
N = 16 Preserves Performance with Fewer Pulses
PRACTICAL CHOICE
N = 16
128 π pulses
−20%
pulse count
+0.97%
sensitivity penalty
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 10

## Slide 11
Hardware Uncertainty Broadens the Preferred Control Depth
400
calibration samples
89%
select N = 12–32
Mode
N=16
22.5% of samples
Uncertainty broadens the preferred depth
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 11

## Slide 12
N = 20 Is the Most Robust Fixed Choice
ALL THREE CRITERIA
N = 20
τ = 1.25 μs
Nominal
95th-percentile regret
Minimum mean regret
p95 regret = 1.154×
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 12

## Slide 13
Measured Hardware Quality Selects the Control Depth
DECISION RULE
(f, Fπ, T₂)
↓
(τ, N, 10% window)
Nominal hardware
τ = 1.25 μs
N = 20 · 160 π pulses
window N = 10–34
Pareto option N = 16
Caveat: contrast, photon rate, overhead and other coherence parameters are held nominal.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 13

## Slide 14
Seven measurements can test the predicted EDT window
FALSIFIABLE TESTS
1
N=16 and N=20 are tied or ordered as predicted
2
N=8 and N=64 are worse than interior controls
3
Measured optimum lies within N=10–34
4
Off-resonance is worse than resonance
5
Values fall within model intervals
Prediction table generated before measurements are entered.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 14

## Slide 15
First-principles data connect material physics to control
The diamond host is fixed, but temperature and strain change the NV transition and relaxation rates used by the control model.
Spin–strain
Udvarhelyi et al.
Six DFT coefficients map axial, transverse and shear strain into the ground-state spin Hamiltonian.
Transition shift
Cambria + Tang
The analytical D(T) law supplies detuning. Tang’s first-principles slope, −75.99 kHz/K, provides an independent cross-check.
Spin–phonon relaxation
Mondal et al.
The ab initio T₁(T) curve constrains the temperature-dependent coherence correction without fitting the EDT optimum.
Temperature + strain
Detuning + T₁/T₂
η(τ,N)
10% region + connected components
Inputs were frozen before the environment scan. No parameter was tuned to the EDT result.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 15

## Slide 16
Environmental detuning moves the optimum without splitting the EDT region
Temperature (K)
CONFIRMED RESULT
Fixed carrier
N = 12
330 K, +20 µε example
Carrier retracked
N = 20
throughout the displayed slice
Topology
β₀ = 1
226 / 226 fine-grid confirmations passed
Environment changes the region’s geometry and recommended depth while its connected-region count stays fixed.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 16

## Slide 17
EDT makes control depth a testable decision
N=20
Resolved optimum
At 200 kHz: τ=1.25 μs and a 10% window spanning N=10–34.
Pulse error
Dominant depth limiter
Removing pulse errors pushes the optimum to the tested boundary.
7 settings
Prospective validation
A minimal experiment can confirm or falsify the predicted window.
Next step: measure the seven-point protocol, update the hardware calibration, then let the decision rule select control depth.
NORTH ATLANTIC TREATY ORGANIZATION
SCIENCE & TECHNOLOGY ORGANIZATION
NATO UNCLASSIFIED RELEASABLE TO STEP Nations and Singapore
13/10/2026 | PAGE 17